## Slide 1
te
Phased Array in Sound
Austin Brummett, EE
Advisor: Dr. Blandford
Abstract
The phased array in sound generates a tone via the STM32F446RE microcontroller that can be phased adjusted by the user through a potentiometer. This creates a sense of directional sound outputting from a line array of speakers which is useful in demonstrating how a phased array system works. Applications of phased arrays are found in many places, such as broadcasting, radar systems, and ultrasonics.
Software Design
Hardware Design
Final Design and Results
This project is tested by having a listener walk across the array to detect a change in the direction of the sound
An oscilloscope was used to prove that the sine waves are phase shifted
Features
Approximately 1 kHz 8-bit sinusoidal output tone sampled at 44.1 kHz via a timer interrupt
Works with any five speakers with internal input amplifiers and a 3.5 mm jack
Adjustable by potentiometer
Five DACs were hooked up to an 8 bit data bus, a chip select bus, and write bus from the STM32F446RE
The DAC’s outputs were sent across a passive RC lowpass filter with a cutoff of approx. 22.1 kHz and then to the speakers via 3.5 mm jack