## Slide 1
Phased Array in Sound
Austin Brummett, EE
Advisor: Dr. Blandford
Abstract
The phased array in sound generates a tone via the STM32F446RE microcontroller that can be phased adjusted by the user through a potentiometer. This creates a sense of directional sound outputting from a line array of speakers which is useful in demonstrating how a phased array system works. Applications of phased arrays are found in many places, such as broadcasting, radar systems, and ultrasonics.
Software Flow Chart
Hardware Flow Chart
Final Design
Features
Approximately 1kHz 8-bit sinusoidal output tone sampled at 44.1kHz via a Timer Interrupt
Works with any five speakers with internal input amplifiers and a 3.5mm jack.
Adjustable by potentiometer.
Final Results
This project is tested by having a listener walk across the array to detect a change in the direction of the sound.
An oscilloscope was used to prove that the sine waves are phase shifted.